## Slide 1: IR LED and Ir transceivers
Gt ece labs
Slides by helen yoo

## Slide 2: What are IR leds and ir transceivers
Infrared light emitting diode
  Lighting device that emits light in infrared range of electromagnetic radiation spectrum
  Not visible to human eyes
  Great for communication
IR Transceivers
  Demodulated output signal directly decoded by microprocessor

## Slide 3: How do they work?
IR LED used to transmit information and IR Transceiver pick out modulated signals
Modulated = unique pattern that transceiver can pick out
Common modulation scheme for IR communication = 38kHz modulation

## Slide 4: 38 kHz modulation
IR LED blinks quickly at a frequency of 38kHz to transmit encoded data
The receiving device demodulates the signal and microcontroller reads a waveform similar to the one on the left