## Slide 1: Schottky Diode
GT ECE academic lab
Slides by Zachary Chan

## Slide 2: Overview
Similar to regular PN junction diodes (only allows current to flow in one direction)
Has advantages and disadvantages
Very useful for switch mode power supplies
Very efficient

## Slide 3: Advantages
Fast switching action
  PN junction struggle to block reverse current when a high frequency (100kHz) is applied
  Schottky diodes can handle frequencies well beyond 100kHz
  Good for high frequency applications such as switch mode power supplies like boost and buck converters
Low voltage drop
  Higher efficiency than regular PN junction diodes
  Does not generate as much heat as PN junction diodes

## Slide 4: Disadvantages
Higher reverse leakage current
  When reverse biased, Schottky diodes allow more current to flow than PN junction diodes which can damage the circuit
Generally costs more

## Slide 5: Component